Analyzing Functions

Implicit Functions and Implicit Differentiation

In mathematics, an implicit function is a generalization of the concept of a function  in which the dependent variable, say,  has not been given "explicitly" in terms of the independent, say,  To give a function explicitly is to be able to express it as By contrast, the function is implicit if the value of  is obtained from by solving an equation of the form

Definition of an Implicit Function

Consider the equation Then

is an implicit function ofin if there exists a function on such that

An implicit function such as can be a useful way to express a functional relationship that may be too complicated, inconvenient or even impossible to solve for  in terms of  For example, the implicit function would be impossible to solve for  in terms of  In another situation, the equation may fail to define a function at all and would express a multi-valued function. For example, the equations , called the Cayley’s Sextic, (see Figure 1) and  called the Tricuspoid (see Figure 2) , express such multi-valued functions, that would be too difficult, if not impossible, to solve for  in terms of

Figure 1                                               Figure 2

In spite of the difficulties in expressing an implicit function explicitly, it is relatively easy to determine its derivative  As an example, determine implicitly, if In determining implicitly, you must think “is a function of”. To emphasize this point, let us suppose that there exists a function  that satisfies the implicit function That is,

Then, we wish to find  Differentiating both sides with respect to we obtain

Exercises: Find implicitly if

Rate of Change

The classic example of a rate of change is that of velocity in rectilinear motion. Consider some object whose motion is on the real line and whose positionat any time from the origin is given by the function called the equation of motion. We are all familiar with the concept of an average velocity in which we compare the change in position with the corresponding change in time by dividing the former by the latter. Thus, if we consider the motion of our object during an interval of time or, we obtain the following definitions:

Average Velocity

Leton

The average velocity during .

From this average, we obtain the concept of an instantaneous velocity at by taking the limit of this average as

Instantaneous Velocity

Leton

The instantaneous velocity at provided this limit exists.

In the same way, we first define the average acceleration  during  Then, from this average, we obtain the concept of an instantaneous acceleration  at by taking the limit of this average as

Instantaneous Acceleration

Leton

The instantaneous acceleration at provided this limit exists.

In comparing two quantities, we do not have to restrict ourselves to position versus time. Realizing that we can compare any two quantities and taking our motivation from the concept of velocity, we can abstract this latter concept of velocity and, thus, derive the concept of an instantaneous rate of change of one quantity with respect to another quantity. Toward this end, consider two quantities functionally related by

Average Rate of Change of the Quantity

Leton

The average rate of change of the quantity with respect to the quantity during .

Instantaneous Rate of Change of the Quantity

Leton

The instantaneous rate of change of the quantity with respect to the quantityat some provided this limit exists.

Examples:

- The surface area  of a sphere of radius is

  - What is the rate of change of the surface of a sphere with respect to its radius

  - What is the rate of change when

  - How must be chosen if the rate of change is

Answers:

.

- .

- For what value of is the rate of change of with respect to  the same as the rate of change of with respect to ? Assumeare constants with

Answer:  We must have:Thus,

Exercises:

- Car A traveling west at 30 mph passes intersection P at noon while car B traveling south at 40 mph passes intersection P three hours later. How fast is the distance between the cars changing at 4:00 p.m.?

- A spot light is on the ground 20 ft away from a wall and a 6 ft tall person is walking towards the wall (See Figure 3).  What is the rate of change of the height of the shadow with respect to the person’s distance from the spotlight at the instant the person is 8 feet from the wall?

Figure 3

- A 15 foot ladder is resting against the wall (See Figure).  The bottom is initially 10 feet away from the wall and is being pushed towards the wall.  How fast is the top of the ladder moving up the wall with respect to the distance the bottom of the ladder is from the base of the wall after bottom has been pushed in three feet?

- Water is being poured into a conical reservoir (Figure 4).  The reservoir has a radius of 5 feet across the top and a height of 14 feet.  At what rate is the volume of the water changing with respect to the radius when the depth is 7 feet? (Hint: By similar triangles See Figure 4)

The volume of water in the reservoir is given by

Figure 4

- A 13-foot ladder is leaning against a vertical wall. If the bottom of the ladder is being pulled away from the wall at the rate of 2 feet per second, how fast is the area of the triangle formed by the wall, the ground and the ladder changing at the instant the bottom of the ladder is 12 feet from the wall?

- Sand is pouring from a pipe at the rate of 16 cubic feet per second. If the falling sand forms a conical pile on the ground whose altitude  is always the diameter of the base  how fast is the altitude increasing when the pile is feet high? Hint: See the Figure and use the fact that the volume.

- An object moves along theaxis. Its position at each  is given by. Determine the

  - (2 pts) formula for the instantaneous velocity.

  - (2 pts) time(s) at which the object is changing direction, if ever.

  - (2 pts) formula for the instantaneous acceleration.

  - (6 pts) time interval(s), if any, during which the object is

| i) speeding up: ______________________________? | ii) slowing down:_____________________________? |
| --- | --- |

- A large balloon is rising at the rate of 20 ft/sec. The balloon is 10 ft above the ground at the point in time that the back end of a car is directly below the bottom of the balloon (see first diagram).  The car is traveling at 40 ft/sec. What is the rate of change of the distance between the bottom of the balloon and the point on the ground directly below the back of the car one second after the back of the car is directly below the balloon (see second diagram)?

Start

After 1 second

- A circle starts out with a radius of 1 cm. (at time and grows for If the area of the circle is increasing at the rate of 2 cm2 per second.

  - Find the rate of change of the radius with respect to time when the radius is 5 cm.

  - What is the radius when

- A sphere is increasing at a rate of 10 in3/sec. Find the radius of this sphere at the moment its surface area is increasing at the rate of 5 in2/sec.

- A fish is reeled in at a rate of 1 foot per second from a point 10 feet above the water.  At what rate is the angle between the fishing line and the water changing when there is a total of 25 feet of fishing line out?

Hint:  Let the amount of fishing line out.

Let the horizontal distance from the fish to the projection of the tip of the fishing pole onto the water.

Let angle between the fishing line and the water.

Given:

Find:

- The dimensions of the cross sections of an isosceles trapezoidal tank consists of  a base of 4 feet, a base of 10 feet, and a height of 12 feet, as shown in the figure below. It is also 100 feet wide (not shown). If the tank is filled by pumping water into it at a rate of 50 cubic feet per minute, how fast is the water level rising when it is 4 feet deep? Hint: The volume of the isosceles trapezoid of water is

- Two people are 50 feet apart.  One of them starts walking north at a rate so that the angle shown in the diagram below is changing at a constant rate of 0.01 rad/min.  At what rate is distance between the two people changing when radians?

Mean Value Theorem

Inequality Preserving Limit Theorem

Let and.

If for all some then

Proof: By contradiction. Assume LetThen since  and there exists a such that, for

From a), b) and c), we obtain, for

This is a contradiction. (

Remark: This theorem is also true for one-sided limits.

Definition of Some Important Points

Letbe defined on an interval I that contains

Definition of a Critical Point

Letbe defined on an interval I that contains

c is a critical point of f a singular point or a stationary point of f.

| Find the critical points ofon |
| --- |
| Derivative of f | Critical Points of f |

Definition of an Absolute Extremum

Let f be defined on an interval I that contains c. Then

has an absolute maximum/max at if

has an absolute minimum/min at if

Definition of a Local Extremum

Let f be defined on an interval I that contains the interior point c. Then

has a local maximum/max atifan open interval

has a local minimum/min ifan open interval

Definition of an End Point Extremum

Let f be defined on an interval I that contains the end point c. Then

has an end point maximum/max at ifa half open subinterval with

has an end point minimum/min at ifa half open subinterval with

Critical Point Theorem (Fermat’s Theorem)

Letbe defined on an interval I.

Ifhas an absolute, local or endpoint extremum atthen c is a critical point of

Proof: We may assume that c is neither an endpoint nor a singular point of; otherwise, we are done.  Therefore c is an interior point of and  exists. Thus, has a local extremum at. We may also assume, without loss of generality, that  has a local maximum at. To finish, we must then show that. So, sincehas a local maximum at an open interval  that contains and is a subset of such thatIn particular,

- .

But, since exists,  Thus, from a) and b), we then obtain that and. Hence, (

Max-Min Existence Theorem (MMT): If f is continuous on the closed interval, then f attains an absolute  maximum and  minimum in .

Remark: If either the ‘continuous’ requirement or the ‘closed interval’ requirement is dropped from the Max-Min Existence Theorem, then the theorem is false. For example,

| Continuity Dropped | Closed Interval Dropped |
| --- | --- |

Example:

| Find the absolute maximum and minimum ofon. |
| --- |
| The Max-Min Theorem guarantees that f attains both a maximum and minimum on and the Critical Point Theorem guarantees that these extrema occur at critical points of f. |
| Critical Points |  |

Exercises:

- Let .

  - State the Max-Min Existence Theorem.

  - State the Critical Point Theorem.

  - Determine the critical points of

  - Determine the absolute maximum and minimum of

Find the absolute maximum and minimum values of in problems 3)-7).

- on

- on

- on

- on

- on

- on

- A model of the velocity of the space shuttle Discovery that deployed the Hubble Space Telescope in 1990 from liftoff at until the solid rocket boosters were jettisoned at seconds is given by Find the absolute maximum and minimum values of the acceleration of the shuttle between liftoff and the jettisoning of the boosters.

Rolle’s Theorem (RT)

Letbe continuous on the closed interval and differentiable on the open interval

If then

Proof:  The theorem is trivial if is constant on. Therefore, we may assume that is not constant on. By the Max-Min Theorem, has both an absolute maximum and absolute minimum on . Clearly, both the maximum and minimum cannot occur at the end points of ; otherwise,  would be constant on . We may therefore assume that has an extremum at some .  By the Critical Point Theorem, since is neither a singular point nor an end point of on , we conclude that   (

Mean Value Theorem (MVT)

Letbe continuous on the closed interval and differentiable on the open interval Then

Proof:  Define where the line determined by the points and Now apply Rolle’s Theorem to on . Therefore, That is,   (

Examples:

- Prove that the equation has exactly one real root.

Proof: Let We will first show that has at least one zero: Applying the Intermediate Value Theorem to on we see that  is continuous onand, Thus,  has at least one real zero in We now show  this is the only real zero of  on By contradiction, assume that has at least two zeros in say,  and with and  Then, by Rolle’s Theorem, But on This is a contradiction . (

- Suppose an object moves in a straight line with position function .  If  is continuous on  and  differentiable onprove its average velocity from to  is taken on as an instantaneous velocity by our object for some

Proof:  The average velocity of  over  is given by  Thus, by the Mean Value Theorem,  (

- If is continuous on and differentiable on with and for all values of   how large can possibly be?

Proof:  By the Mean Value Theorem, we have for some  This implies that Thus,  (

Monotonicity

| Definition of a Strictly Monotonic Function |
| --- |
| Let f be defined on an interval I. Let and |
| f is increasing on I if |  |
| f is decreasing on I if |  |

Monotonicity Theorem

Let f be continuous on an interval I and differentiable on the interior of I.

Proof of (i): Let with To show Apply the MVT to on Therefore, there exists some such that  Since and we have that or Thus,   (

Proof of (ii): Let with To show Apply the MVT to on Therefore, there exists some such that  Since and we have that or Thus,   (

Proof of (iii): Let with To show May assume that  Apply the MVT to on Therefore, there exists some such that  Since and we have that or Thus, since were arbitrary,   (

Corollaries

Let f , g be continuous on an interval I and differentiable on the interior of I. Then

Monotonic Endpoint Extension Theorem

Let f be continuous at and monotonic on the open interval.Then

f is monotonic on the closed interval .

Proof:  Without loss of generality, we may assume that on( if on , consider ) .  Let . To show that. Choose with . Let . Then

Since  on, we have, for ,

By the Inequality Preserving Limit Theorem and the continuity of  at ,  we have

(*)

Since , we have from (*)

Thus, . (

| Find where and where |
| --- |
| We use the Monotonicity Theorem to construct the Sign Chart of |
| Thus on and | Sign Chart of |
|  | 0 0 0 |

Find whereand where

We use the Monotonicity Theorem to construct the Sign Chart of

Sign Chart of 0 ND 0

The Sign Chart tells us that and on

Find where and where

We use the Monotonicity Theorem to construct the Sign Chart of

Sign Chart of 0 0

The Sign Chart tells us that and on

Find whereand where

We use the Monotonicity Theorem to construct the Sign Chart of

Sign Chart of 0 0

The Sign Chart tells us that on and

Find whereand where

We use the Monotonicity Theorem to construct the Sign Chart of

Sign Chart of 0 ND

The Sign Chart tells us that and on

Speeding Up/Slowing Down Theorem

Consider some object in rectilinear motion on the real line with position and velocity

during the interval of time . Let be continuous on and

differentiable on . Then

1. If and on , then The object is Speeding Up on . The object is moving Toward the Left on .

If and on , then The object is Speeding Up on . The object is moving Toward the Right on .

If on and on , then The object is Slowing Down on . The object is moving Toward the Right on .

If on and on , then The object is Slowing Down on . The object is moving Toward the Left on .

Proof:  We shall only prove case 1, since the other cases have a similar proof. Now since on , by the Monotonicity Theorem, . Thus, on . This says our object is speeding up on .  Again, by the Monotonicity Theorem, since  on , on . This says our object is moving toward the left on .

Concavity

Definition of Concavity

Let f be differentiable on an open interval

Concavity Theorem

Let f be twice differentiable on an open interval I.

Find where is concave up and where it is concave down.

We use the Concavity Theorem to construct the Sign Chart of

Sign Chart of

Definition of an Inflection Point

Let f be continuous at

Critical Point Theorem for Inflection Points

Let be an inflection point of Then

is a critical point of that is, or is not defined.

Proof: Assume it is not the case that is not defined. Therefore  exists and, hence,  is continuous at c. Now since is an inflection point of f,We may assume without loss of generality that . Therefore  because is continuous at Thus. Sinceexists, this implies that  as in the proof of the Critical Point Theorem.

| Find the Inflection Points of |
| --- |
|  | Inflection Points Possibly Occur at |
| We use the Concavity Theorem to construct the Sign Chart of |
| Sign Chart of |
| The Sign Chart tells us that an inflection point occurs at |

| Find the Inflection Points of |
| --- |
|  | Inflection Points possibly occur at |
| We use the Concavity Theorem to construct the Sign Chart of |
| Sign Chart of |
| The Sign Chart tells us that inflection points occur at. |

| Find the Inflection Points of |
| --- |
|  | Inflection Points possibly occur at |
| We use the Concavity Theorem to construct the Sign Chart of |
| Sign Chart of |
| The Sign Chart tells us that an inflection point occurs at |

Sign Preserving Limit Theorem

Let Then

such that keeps the same sign as

Proof: LetThen, since, there exists a such that

.

Case

Case   (

Remark: This theorem is also true for one-sided limits.

First Derivative Test Theorem

Let be continuous on an open intervalthat contains the critical point c. Then

on and on is a local maximum.

on and on is a local minimum.

keeps the same sign on both sides of is not a local extreme value.

Proof of (i): Assume  on  and  on Since  f is continuous on both and, we have by the Monotonicity Theorem thaton  and Thus,  is a local maximum on . (

Proof of (ii): Assume  on  and  on  Since  f is continuous on both and, we have by the Monotonicity Theorem thaton  and Thus,  is a local minimum on . (

Proof of (iii): Similar to the proofs of (i) and (ii), in which we either have on  or on. Thuscan not be a local extreme value.  (

Second Derivative Test Theorem

Suppose and exists. Then

is a local minimum.

is a local maximum.

Proof of (i): Assume. So  is continuous at c.  Since such that , when  or  Thus,

by the First Derivative Test,  is a local minimum.

Proof of (ii): Assume. So  is continuous at c.  Since such that ,  when  or Thus,

by the First Derivative Test,  is a local maximum. (

Exercises:

- One end of a 27-foot ladder rests on the ground and the other end rests on the top of an 8-foot wall. As the bottom of the ladder is pushed along the ground toward the wall, the top extends beyond the wall. Find the maximum horizontal overhang of the top end (see Figure 6).

Figure 6

- Find the coordinates ofthat maximizes the area of the rectangle shown in the figure below.

- A rectangular piece of paper is 12 inches high and six inches wide. The lower right-hand corner is folded over so as to reach the leftmost edge of the paper (See figure.). Find the minimum length of the resulting crease.

- Find the point  on the graph of  that is nearest to the point by determining the following, where S denotes the function that is to be minimized.

  - Critical points of

  - Test the Critical Points:

  - Answer:  the point  on the graph of  that is nearest to the point

- An advertising flyer is to contain 50 square inches of printed matter, with 2-inch margins at the top and bottom and 1-inch margins on each side. What dimensions for the flyer would use the least paper?

- An advertising flyer is to have an area of 50 square inches, in which the printed matter will have 2-inch margins at the top and bottom and 1-inch margins on each side. What dimensions for the flyer would maximize the printed matter?

- The graph of is a "tilted" ellipse (See diagram.). Among all points (x, y) on this graph, find the largest and smallest values of y. Among all points (x, y) on this graph, find the largest and smallest values of x.

- Problem: There are infinitely many lines that pass through the point  and form a right triangle with the coordinate axes (see the accompanying figure). In this problem, you are to justify the existence of that line through that minimizes the area of the right triangle thus formed by answering the following questions:

- State the Max-Min Theorem (MMT).

- Determine a function  that expresses the area of any of the right triangles formed by the axes and a line that passes through.

- Determine the domain Dom

- Apply MMT to

- A humidifier uses a rotating disk of radius  which is partially submerged in water (shown in the lower region of the figure labeled WATER). The most evaporation occurs when the exposed wetted region (shown as the upper region of the figure labeled WETTED) is maximized. Show this happens when  (the displacement from the center to the water) is equal to .

- The function has a local minimum at  and satisfies  Find    and

- What are the dimensions and the volume of the square pyramid that can be cut and folded from a square piece of cardboard 20 by 20 square inches as illustrated in Figure 4 so that its volume is a maximum?

Figure 4

- What are the dimensions and the volume of the square pyramid that can be cut and folded from a square piece of cardboard 20 by 20 square inches as illustrated in Figure 5 so that its volume is a maximum?

Figure 5

- Which of the two constructed square pyramids from the above problems has the larger volume?

Asymptotes

Definition of a Horizontal Asymptote (H.A.)

Find the horizontal asymptotes of

Sign Chart of 0 ND

The line is an H.A. and

Definition of a Vertical Asymptote (V.A.)

Find the vertical asymptotes of

Sign Chart of 0 ND

The line is a V.A. and

Definition of an Oblique Asymptote (O.A.)

Find the oblique asymptotes of

The line is an O.A.

Find the oblique asymptotes of

The line is an O.A.

Find the horizontal asymptotes of

Sign Chart of

The line is an H.A. and

Find the horizontal asymptotes of

Sign Chart of 0 ND

The line is an H.A. and

Find the vertical asymptotes of

Sign Chart of 0 ND

The line is a V.A. and

Curve Sketching

Sketch the graph of

0 0 ---0 ---------- 0 -----------------------------------------0---

Sketch the graph of

-------------------------------------- 0 0 ----------------------------- 0 0 --------- --------------

Sketch the graph of.

0 ND --------- 0 ND -------------------0------------ 0 ND ------------------------------- 0

Antiderivatives

Most mathematical operations have anti operations. In algebra, for example, the anti operation of multiplication is division, that of addition is subtraction, and that of raising to a power is taking a root. More commonly, these anti operations in algebra are called inverse operations. As you can see, each anti operation undoes the original operation. In the Calculus, the anti operation of differentiation (finding the derivative) is called antidifferentiation or integration. The result of an application of antidifferentiation   is called an antiderivative. For example, since we say that is an antiderivative of we say that is an antiderivative of Please note that antiderivatives are not unique. For example, we also have  So, is also an antiderivative of

Definition of an Antiderivative

Letbe continuous on an interval

is an antiderivative of on if is continuous onandon the interior of

By a previous corollary to the Mean Value Theorem (MVT), if on an intervalthen and must differ by some constant on That is, on for some constant Therefore, if is an antiderivative of on  the most general antiderivative of on is given by on for some constant Since  denotes differentiation with respect to we will at times suggestively use to denote antidifferentiation with respect to  Thus,   on  Even though the notation is most reasonable, this is not the  notation that is universally used to denote the general antiderivative. This latter notation is reserved for or and is due to Leibniz.

Definition of the General Antiderivative or Indefinite Integral

Letbe continuous on an interval

We denote by the indefinite integral (general antiderivative) of on Then, if is an arbitrary constant, called the constant of integration,

if on

See Figure 7 for a graphic description of the relationship between integration and differentiation.

Figure 7

Stated in another way,

Basic Table of Indefinite Integrals

- ℝ

- where

Proof:   (

Linearity of the Indefinite Integral

Let ℝ. Then

Definition of the Differential

Leton

The differentialon if on

Let  Using the Differential, we may write

Example:

Differential Equations

Def: A differential equation is an equation involving the independent variable x, the dependent variable y and the latter’s derivatives expressed as  Our goal is to solve such an equation; that is, to find a function such that it and its various derivatives satisfy this equation. We will study a type of differential equation called a first order separable differential equation. This is the type in which only the variablesappear and in which the expressions involving the variable x can be separated to one side of the equal sign and the expressions involving the variable y can be separated to other side of the equal sign. This separation is accomplished most easily by using differentials.

Examples:

- Find the xy-equation of the curve through  whose slope at any point is the ratio of its first coordinate to its second

coordinate.

Solve:

What is C? This latter equation implies,

using our initial condition, that

Thus,

Answer:

- Find  such that  and

Solve: 	What is C?  Then, as before,

Thus,

Answer:

- Find the equation of motion of an object moving vertically near the surface of Planet X with initial velocity  and  a  height

from the surface. Planet X has an acceleration due to gravity of

Solve:

What is? Then, as before,

Thus, so far, Again,

What is?

Then, as before,

Answer:

If the object is dropped, then  and the solution becomes

If the object is on the surface of Planet X, then  and the solution becomes

If Planet X is the Earth, then / second2.

Remark: To every differentiation rule there corresponds a differential rule. For example, to the product rule there corresponds the differential rule

# Footnotes

We must allow both and when considering averages and limits. However, to save space we will usually only illustrate the case in which.

We will frequently use the phrase “rate of change” without modifier to mean “instantantaneous rate of change”.

Similar proof ifhas a local minimum at.

Similar proof if